# Text boxes

1 – INTAKE COVER W/ SCREEN/RING ASSEMBLY

1 – K&N® VENTURI AIR FILTER

1 – MOUNTING PLATE

1 – BILLET VELOCITY STACK

1 – THROTTLE BODY COVER

2 – INTAKE GASKET

2 – BREATHER BOLT, 3/8”-16 X 1” W/ TEFLON SEALANT

3 – BOLT, 1/4”-20 X 1-1/8”, BUTTONHEAD W/ LOCK PATCH

3 – LOCK WASHER, 1/4” TOOTHED

5 – BOLT, 1/4"-20 X 1/2", BUTTONHEAD W/ LOCK PATCH

# Items Supplied >

Read all instructions carefully and completely before installing your new air intake.

- Remove the allen bolt from the center of the stock air cleaner and remove the cover. Remove the (3) bolts securing the filter to the throttle body and remove the filter and breather hose assembly. Save the stock breather hose assembly as this will be reused. Remove the two breather bolts from the cylinders and remove the back cover.

- Install the supplied breather bolts into the cylinders. See FIGURE 1. Tighten securely.

- Insert the center hose of the stock breather hose assembly through the hole in the supplied mounting plate and then through the velocity stack so that the hose is in the center of the velocity stack. See FIGURE 1 & 2.

- While holding that assembly together with one hand, Insert the (3) supplied 1/4”-20 x 1-1/8” buttonhead bolts and lock washers through the mounting holes in the velocity stack and mounting plate. See FIGURE 1.

- Then align the supplied gaskets and spacer so the notch is to the bottom left and slide them over the (3) bolts onto the backside of the mounting plate. Make sure there is a gasket on both sides of the spacer. See FIGURE 1.

- Align all the components with the throttle body and start threading the (3) buttonhead bolts into the throttle body. Tighten the three bolts evenly making sure the inner diameter of the velocity stack, gaskets, and spacer align with the inner diameter of the throttle body.

- Attach the stock breather hoses to the breather bolts in the cylinder head. The front hose has to go behind the mounting plate to be attached to the breather bolt.

- Install the throttle body cover using the (2) 1/4-20 X 1/2” button head screws as shown in FIGURE 1 &2.

- Place the supplied K&N® filter onto the velocity stack. See FIGURE 3.

- Insert the intake screen into the intake ring so the screen sits inside the edge of the ring. See FIGURE 3.

- Place the ring and screen between the legs of the intake cover as shown in FIGURE 3.

- Place the intake cover, ring, and screen assembled in previous step over the air filter and align each leg to the base mounting plate threaded holes. Be sure screen sits at a 45° angle to the bottom leg, and C/V logo'd leg is at the upper left position. See FIGURE 3.

- Insert the (3) supplied 1/4"-20 x 1/2” buttonhead bolts through the intake cover and into the base mounting plate, see FIGURE 3. Double check all parts are aligned properly and tighten securely.

- Verify all the bolts are tight and then wipe off any fingerprints with a clean microfiber cloth.

# Instruction Manual >

606-0101-01/02/03/04

DISCLAIMER: NOT LEGAL FOR SALE OR USE IN CALIFORNIA ON ANY POLLUTION CONTROLLED MOTOR VEHICLES.

HARLEY:

DRESSER				2017

NOTE: DOES NOT FIT CVO MODELS.

# Application(s) >

INTAKE SPACER

SUPPLIED INTAKE GASKET

ASSEMBLY FROM STEPS 3-5

C/V LOGO’D LEG

POSITIONED

HERE

Document No.  0017	REV. A

Page 1 of 3

INTAKE RING

Page 3 of 3

FIGURE 3

STOCK BREATHER HOSE

CONTINUED ON PAGE 2

606-0101-01/02/03/04

POSITION NOTCH IN SPACER AND GASKET AS SHOWN

Document No.  0018	REV. B

# Instruction Manual >

(3) 1/4”-20 x 1/2” BUTTONHEAD BOLTS

K&N® VENTURI AIR FILTER

CONTINUED ON PAGE 3

THROTTLE BODY COVER

INTAKE SCREEN

DISCLAIMER: NOT LEGAL FOR SALE OR USE IN CALIFORNIA ON ANY POLLUTION CONTROLLED MOTOR VEHICLES.

INTAKE COVER

(NOTE: DESIGN WILL VARY BASED ON PART NUMBER)

TOP 12-POINT BOLT

SHOULD BE CENTERD

AS SHOWN

FIGURE 2

CENTER  BREATHER HOSE

(2) 1/4”-20 x 1/2” BUTTONHEAD BOLTS W/  LOCK PATCH

### FIGURE 1

(3) 1/4”-20 x 1-1/8” BUTTONHEAD BOLTS W/  LOCK PATCH

# Instruction Manual >

606-0101-01/02/03/04

Page 2 of 3

Document No.  0018	REV. B

(3) LOCK WASHERS

VELOCITY STACK

SUPPLIED INTAKE GASKET

(2) SUPPLIED BREATHER BOLTS W/ TEFLON SEALANT

STOCK  BREATHER HOSES

MOUNTING PLATE

THROTTLE BODY COVER